## Slide 1: CES Integrated Digital Cockpit Demo
Proposed Development Plan

## Slide 2: Digital Cockpit Architecture – Full Details
IVI UI
Qt
OS / Linux
Type 1 Hypervisor (SC)
SoC
Cluster UI
Qt
Tell-tales
Qt Safe Renderer
ASIL-D RTOS
ASIL-B
There is a 3rd video layer needed by the cluster screen and that is for functional safety. The Qt Safe Renderer draws the safety critical part that includes the telltales and is largely transparent as illustrated by the dark blue outlined layer. The non-safety critical dials and other driver specific information is also drawn by the ASIL domain as illustrated by the green outlined layer.
Portions of the non-safety layer are transparent to allow the IVI functionality to be displayed in the case where there is a 3rd plane underneath for the IVI layer that spans all displays.
A complication is that there could be different cluster modes where the size of the dials change and with it the area available to the IVI content. This implies a communication channel between the IVI and cluster domains to signal these configuration changes.
There should be a fallback cluster configuration in the event the IVI domain fails.
Safety critical graphics plane
Non safety critical graphics plane
IVI Content graphics plane

## Slide 3: Step 1: Desktop Development
Develop this screen with telltales using the Qt Safe Renderer Tooling
Provide input for
  speed
  speed limit value (comes from navigation system we hope)
  electric power use
  drive train status (PRND)
  Tell tales (actual ones TBD – Johan?)

## Slide 4: Step 1: Tasks and missing details
Need to know tell-tale design – Johan?
Nice to have 3D design input to create needles. Even better if can use Qt 3D Studio. Ask Sami.
Design API for getting data into the cluster. Work with Kalle’s team. Timo is working on this. See https://bugreports.qt.io/browse/QTPM-928, https://bugreports.qt.io/browse/QTAUTO-570

## Slide 5: Step 2: Intermediate Architecture
Build on Intel NUC
Cluster in independent process, rendering to separate layer
IVI graphics layer is below cluster layer
Layers composited by the graphics hardware
IVI UI
Linux
SoC
Cluster UI

## Slide 6: Step 2: Tasks
Get the IVI code from Luxoft and get running on the NUC
Luxoft owns the IVI code. To be investigated is if we can help on some apps, e.g. car status
Figure out how to configure graphics layers on the NUC
Run the Cluster as a separate process displaying on another graphics layer than IVI

## Slide 7: Step 3: Final CES Architecture
GHS Multivisor
Renesas H3
IVI UI
Linux
Multivisor
SoC
Cluster UI
QSR
INTEGRITY

## Slide 8: Step 3: Tasks
Requires Kalle’s team to get Qt running on the INTEGRITY T17 and integrated with Renesas software package
  https://bugreports.qt.io/browse/QTPM-767
  https://bugreports.qt.io/browse/QTPM-869
Assume no help from Luxoft in this part